## Slide 1: OpenvSwitch L7 matchers & conntrack metadatas
Open vSwitch conference, November 2014
Franck Baudin

## Slide 2: L7 classification insights: functional
L7 classification is based on network conversations analysis
  Conversation: (client -> server) and (server -> client)
    2 OpenFlow flows
  Direct mapping on Linux: conntrack
L7 classification is based on payload
  IP reassembly
  TCP segment reordering
Most applications are classified with the first packet of payload
  … so right after TCP handshake
  some applications requires more packets (skype, bittorrent, …)
  Signalization protocols generating RELATED conversations to be analyzed even if classified (ex: ftp & ftpdata)
  If the application is not recognized after N packets: classified as “unknown”

## Slide 3: L7 classification insights: performances
At a given time, 10% of the traffic is under L7 classification, 90% is already classified
  Return of experience from carriers: typical value on a Gi interface
  Offloading (bypass when classified) is key for performance
On Intel E5-2680@2.70GHz, per core (2HT) : ~4Gbps, 10k conversation/s

## Slide 4: L7 workflow
CT
NFQ
recirc
CT->mark=0
L7 engine
(2) async update:
set(CT_ID, mark=value)
packet copy/reference + CT_ID
user
kernel
CT->mark=5
output, drop, QoS, …
in_port=1
L7 matcher
L2-L4 matcher

## Slide 5: L7 rule-set hierarchy
CT
NFQ
goto
Low*
bittorrent
output, drop, QoS, …
in_port=1
skype
output, drop, QoS, …
in progress
in_port=1
output, drop, QoS, …
High priority rule
Medium priority rules
Low* priority rules
L7 matcher
L2-L4 matcher

## Slide 6: Rule-set example
# Assuming that (conn_mark == 0) when (skb->CT == NULL)
in_port=1,priority=50000,conn_mark=0,actions=conntrack(),nfqueue(2),goto_table:128
# conn_mark !=0: flow has been analyzed, and this is the final verdict for the flow.
in_port=1,priority=40000,conn_mark=27,actions=…
in_port=1,priority=40000,conn_mark=55,actions=…
in_port=1,priority=40000,conn_mark=10,actions=…
…
# L2-L4 catch all rules, including “unknown L7” and “L7 classification in progress”
table=128,in_port=1,tcp,tp_dst=80,actions=…
table=128,in_port=1,icmp,actions=…
…

## Slide 7: Beyond L7 classification: per flow metadatas
Add a new conntrack field instead of using ct->mark
  uint32_t ct->regs[NF_CONNTRACK_MAX_REGS = 4]
User can store
  L7 classification(s)
  Subscriber ID, SLA ID
  Policy ID to apply
  NSH service path, service index, metadatas, …
  “Global conntrack UUID” in case of a “HA distributed firewall/NAT”
  …
OpenFlow extension
  matcher: conn_register[]
  actions: reuse of conn_register[] value for NSH encapsulation

## Slide 9: Rule-set alternate example
# in order keep CT updated, assuming that conn_mark is unusable when (skb->ct == NULL)
in_port=1,priority=50000,actions=conntrack(),recirc
# conn_mark==0 means that L7 classification is in progress, keep feeding the L7 engine
in_port=1,priority=49999,conn_mark=0,actions=nfqueue(2),goto_table:128
# conn_mark !=0: flow has been analyzed, and this is the final verdict for the flow.
in_port=1,priority=40000,conn_mark=27,actions=…
in_port=1,priority=40000,conn_mark=55,actions=…
in_port=1,priority=40000,conn_mark=10,actions=…
…
# L2-L4 catch all rules, including “unknown L7” and “L7 classification in progress”
table=128,in_port=1,tcp,tp_dst=80,actions=…
table=128,in_port=1,icmp,actions=…
…