## Slide 1: Measuring OVS Performance
Framework and Methodology
Vasmi Abidi, Ying Chen, Mark Hamilton
vabidi@vmware.com, yingchen@vmware.com

## Slide 2: Agenda
Layered performance testing methodology
  Bridge
  Application
Test framework architecture
Performance tuning
Performance results
Notes: We address only kernel data path.
No punts to user space

## Slide 3: What affects “OVS Performance”?
Unlike a Hardware switch, performance of OVS is dependent on its environment
CPU Speed
  Use a fast CPU
  Use “Performance Mode” setting in BIOS
  NUMA considerations e.g. number of cores per NUMA node
Type of Flows (rules)
  Megaflows rules are more efficient
Type of traffic
  TCP vs UDP
  Total number of flows
  Short-lived vs long-lived flows
NIC capabilities
  Number of queues
  RSS
  Offloads – TSO, LRO, cksum, tunnel offloads
vNIC Driver
  In application-level tests, vhost may be bottleneck

## Slide 4: Performance Test Methodology
Bridge Layer

## Slide 5: Bridge Layer: Topologies
OVS
Linux Host
L2 Switch Fabric
Spirent Test Center
Port1
Tx
Port2
Rx
Topology1 is a simple loop through hypervisor OVS
Topology2 includes tunnel between Host0 and Host1
No VMs in these topologies
Can simulate VM endpoints with physical NICs
Host0
OVS
Host1
OVS
L2 Switch Fabric
Spirent Test Center
Port1
Tx
Port2
Rx
Simple loopback
Simple Bridge
Topology2
Topology1
Notes: Audience Q: What does bullet#3 mean?

## Slide 6: Bridge Layer: OVS Configuration for RFC2544 tests
Test Generator wizards typically use configurations (e.g. ‘learning phase’) which are more appropriate for hardware switches
For Spirent, there is an non-configurable delay between learning phase and test phase
Default flow max-idle is shorter than the above delay
  Flows will be evicted from kernel cache
Flow miss in kernel cache affects measured performance
Increase the max-idle on OVS
ovs-vsctl set Open_Vswitch . Other_config:max-idle=50000
Note: this is not performance tuning. It is to accommodate the test equipment’s artificial delay after the learning phase

## Slide 7: Performance Test Methodology
Application Layer

## Slide 8: Application-based Tests Using netperf
VM1
OVS2
Host0
Host1
L2 Switch Fabric
KVM
KVM
OVS1
VM8
VM1
VM8
netperf in VM1 on Host0 connects to netserver on VM1 on Host1
Test traffic is VM-to-VM, upto 8 pairs concurrently, uni and bidirectional
Run different testsuites: TCP_STREAM, UDP_STREAM, TCP_RR, TCP_CRR, ping

## Slide 9: Logical Topologies
Bridge – no tunnel encapsulation
STT tunnel
VXLAN tunnel

## Slide 10: Performance Metrics

## Slide 11: Performance Metrics
Throughput
  Stateful traffic is measured in Gbps
  Stateless traffic is measured in Frames per Second (FPS)
    Maximum Loss Free Frame Rate as defined in RFC2544 (MLFFR)
    Alternatively, Tolerate Frame Loss Threshold, e.g. 0.01%
Connections Per Second
  Using netperf –t TCP_CRR
Latency
  Application level round-trip latency in usec using netperf –t TCP_RR
  Ping round-trip latency in usec using ping
CPU Utilization
  Aggregate CPU Utilizations on both hosts
  Normalized by Gbps

## Slide 12: Measuring CPU Utilization
Tools like top under-report for interrupt-intensive workloads
We use perf stat to count cycles & instructions
Run perf stat during test
  perf stat -a -A -o results.csv -x, -e cycles:k,cycles:u,instructions sleep <seconds>
Use nominal clock speed to calculate CPU % from cycle count
Record cycles/instruction

## Slide 13: What is “Line rate”?
Maximum rate at which user data can be transferred
Usually less than raw link speed
because of protocol overheads
Example: VXLAN-encapsulated packets

## Slide 14: Performance Metrics: variance
Determine variation from run to run
Choose acceptable tolerance

## Slide 15: Testing Architecture

## Slide 16: Automation Framework Goals & Requirements
Provide independent solutions to do:
  System setup and baseline
  Upgrade test components
  Orchestration of Logical network topology, with and without Controllers
  Manage tests and execution
  Report generation - processing test data
Provide system setup and baseline to the community
  System configuration is a substantial task
Leverage open source community
100% automation

## Slide 17: Automation Framework: Solutions
Initial system setup and baseline Ansible
  Highly reproducible environment
  Install a consistent set of Linux packages
  Provide template to the community
Upgrade test components Ansible
  Installing daily builds onto our testbed e.g. openvswitch
Logical network topology configuration Ansible
  Attaching VMs and NICS, configure bridges, controllers, etc
Test management and execution Ansible, Nose, Fabric
  Support hardware generators Testcenter Python libraries
  netperf
  Extract system metrics
Report generation, validate metrics django-graphos & Highchart
Save results Django

## Slide 18: Framework Component: Ansible
Ansible is a pluggable architecture for system configuration
  System information is retrieved then used in a playbook to govern changes that are applied to a system
Already addresses major system level configuration
  Installing drivers, software packages etc across various Linux Flavors
Agentless – needs only ssh support on SUT (System Under Test)
Tasks can be applied to SUTs in parallel, or forced to be sequential
Rich template support
Supports idempotent behavior
  OVS is automation-friendly, because of CRUD behavior
It’s essentially all Python – easier to develop and debug
Our contributions to Ansible: modules openvswitch_port, openvswitch_bridge, openvswitch_db
Ansible website http://www.ansible.com/home

## Slide 19: Performance Results

## Slide 20: System Under Test
Dell R620 2 sockets, each with 8 cores, Sandy bridge
Intel Xeon E5-2650v2 @ 2.6GHz, L3 Cache 20MB, mem 128GB
Ubuntu 14.04 64-bit with several system level configurations
OVS version 2.3.2
Use kernel OVS
NIC - Intel X540-AT2 ixgbe version 3.15.1-k
  16 queues, because there are 16 cores
(Note: # of queues and affinity settings are NIC-dependent)
Notes: E5-2650 v2
L3 Cache 20MB
“several system level configs” - which ones
Remove NSX version
OVS build is internal. Won’t be understood by external audience.
“stock driver” – give version
16 rx queues and 16 tx qeueues?
mention 1:1 mapping between queues and cores
Irqbalance disabled? Interrupt moderation?
Affinity settings
NIC MTU?
Queue sizes?
remove last bullet

## Slide 21: Testbed Tuning
VM Tuning
  Set cpu model to match the host
  2 MB huge pages, no sharing locked
  Use ‘vhost’, a kernel backend driver
  2 vCPU, with 2 vnic queues
Host tuning
  BIOS is in “Performance” mode
  Disable irqbalance
  Affinitize NIC queues to cores
  Set swappiness to 0
  Disable zone reclaim
  Disable arp_filter
VM XML
<cpu mode='custom' match='exact'>
<model fallback='allow'>SandyBridge</model>
<vendor>Intel</vendor>
</cpu>
<vcpu placement='static’>2</vcpu>
<memtune>
<hard_limit>2097152</hard_limit>
</memtune>
<memoryBacking>
<hugepages/>
<locked/>
<nosharepages/>
</memoryBacking>
<driver name='vhost' queues='2'/>
Host /etc/sysctl.conf
vm.swappiness=0
vm.zone_reclaim_mode=0
net.ipv4.conf.default.arp_filter=1
Notes: remove “new” from title.
VM tuning does not apply to hardware tests
Vhost-net multiqueue used in VM?

## Slide 22: Bridge Layer: Topologies
OVS
Linux Host
L2 Switch Fabric
Spirent Test Center
Port1
Tx
Port2
Rx
Topology1 is a simple loop through hypervisor OVS
Topology2 includes tunnel between Host0 and Host1
No VMs in these topologies
Can simulate VM endpoints with physical NICs
Host0
OVS
Host1
OVS
L2 Switch Fabric
Spirent Test Center
Port1
Tx
Port2
Rx
Simple loopback
Simple Bridge
Topology2
Topology1
Notes: Audience Q: What does bullet#3 mean?

## Slide 23: Bridge Layer: Simple Loopback Results
1 and 8 cores NUMA results only use cores on the same NUMA node as the NIC
Throughput scales well per core
Your mileage may vary depending on system, NUMA architecture NIC manufacturer etc.
Chart: Throughput (KFPS) vs Frame Size for Loopback
| 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 1514.0
1 core NUMA | 1053.5001 | 1055.7433 | 1045.9974 | 1008.0646 | 1004.8232 | 811.7476
8 cores NUMA | 6009.6154 | 5956.6729 | 4528.9856 | 2349.6241 | 1197.3181 | 813.8021
16 cores | 11565.6824 | 8445.946 | 4528.9856 | 2349.6241 | 1197.3181 | 813.8021
Chart: Throughput (Gbps) vs Frame Size for Loopback
| 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 1514.0
1 core NUMA | 0.70795 | 1.25 | 2.3096 | 4.2903 | 8.3923 | 9.9618
8 cores NUMA | 4.0385 | 7.0527 | 10 | 10 | 10 | 9.987
16 cores | 7.7721 | 10 | 10 | 10 | 10 | 9.987

## Slide 24: Bridge Layer: Simple Bridge Results
For 1-core and 8-core cases, CPUs are on same NUMA node as NIC
Results are similar to simple loopback
Ymmv. Depends on system architecture, NIC type, …
Chart: Throughput (KFPS) vs Frame Size Simple Bridge
| 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 1514.0
1 core NUMA | 1011.3269 | 818.0629 | 820.21 | 783.2081 | 785.1759 | 785.1759
8 cores NUMA | 5896.2265 | 4464.2858 | 4528.9856 | 2349.6241 | 1197.3181 | 813.8021
16 cores | 11283.5166 | 8445.946 | 4528.9856 | 2349.6241 | 1197.3181 | 813.8021
Chart: Throughput (Gbps) vs Frame Size for Simple Bridge
| 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 1514.0
1 core NUMA | 0.67961 | 0.96859 | 1.811 | 3.3333 | 6.5578 | 9.6357
8 cores NUMA | 3.9623 | 5.2857 | 10 | 10 | 10 | 9.987
16 cores | 7.5825 | 10 | 10 | 10 | 10 | 9.987

## Slide 25: Application-based Tests
VM1
OVS2
Host0
Host1
L2 Switch Fabric
KVM
KVM
OVS1
VM8
VM1
VM8
netperf in VM1 on Host0 connects to netserver on VM1 on Host1
Test traffic is VM-to-VM, upto 8 pairs concurrently, uni and bidirectional
Run different testsuites: netperf TCP_STREAM, UDP_STREAM, TCP_RR, TCP_CRR, ping

## Slide 26: netperf TCP_STREAM with 1 VM pair
  Conclusions
  for 64B, sender CPU bound
  for 1500B, vlan & stt are sender CPU bound
  vxlan throughput is poor. Because no hw offload, CPU cost is high
 | Throughput | 
Topology | Msg Size | Gbps
stt | 64 | 1.01
vxlan | 64 | 0.70
vlan | 64 | 0.80
stt | 1500 | 9.17
vlan | 1500 | 7.03
vxlan | 1500 | 2.00
stt | 32768 | 9.36
vlan | 32768 | 9.41
vxlan | 32768 | 2.00
Notes: Can remove table, since info is in the chart
With small msg-size, is TCP_NODELAY used (no, for single session)? What’s the pkt size which OVS sees (250B maybe)?
CPU 200%. In host or VM?
Affinity and NUMA considerations

## Slide 27: netperf TCP_STREAM with 8 VM pairs
  Conclusions:
  For 64B, sender CPU consumption is higher
  For large frames, receiver CPU consumption is higher
  For given Throughput, compare CPU consumption
 | Throughput 8 VMs | 
Topology | Msg Size | Gbps
vlan | 64 | 6.70
stt | 64 | 6.10
vxlan | 64 | 6.48
vlan | 1500 | 9.42
stt | 1500 | 9.48
vxlan | 1500 | 9.07

## Slide 28: netperf bidirectional TCP_STREAM with 1 VM pair
  Conclusion:
  Throughput is twice unidirectional
Bidirectional Throughput 1 VMs |  | 
Topology | Msg Size | Gbps
stt | 64 | 2.89
vlan | 64 | 3.10
stt | 1500 | 17.20
 | 1 VM | CPU (%)/Gbps | 
Topology | Msg Size | Host 0 | Host 1
vlan | 64 | 121 | 121
stt | 64 | 167 | 155
stt | other | 15 | 15

## Slide 29: netperf bidirectional TCP_STREAM with 8 VM pairs
  Note:
  Symmetric CPU utilization
  Large frames, STT utilization is the lowest
Bidirectional Throughput 8 VMs |  | 
Topology | Msg Size | Gbps
vlan | 64 | 17.85
stt | 64 | 17.3
vlan | 1500 | 18.4
vlan | 1500 | 18.7
 | 8 VM | CPU (%)/Gbps | 
Topology | Msg Size | Host 1 | Host 2
vlan | 64 | 69 | 69
stt | 64 | 75 | 75
vxlan | 64 | 118 | 118
vlan | 1500 | 65 | 65
stt | 1500 | 53 | 53

## Slide 30: Testing with UDP traffic
UDP results provide some useful information
  Frame per second
  Cycles per frame
Caveat: Can result in significant packet drops if traffic rate is high
  Use packet-generator that can control offered load, e.g. ixia/spirent
  Avoid fragmentation of large datagrams

## Slide 31: Latency Using netperf TCP_RR
Transactions/sec for 1-byte request-response over persistent connection
Good estimate of end-to-end RTT
Scales with number of VMs

## Slide 32: CPS Using netperf TCP_CRR
Chart: CPS vs Number of VMs and Sessions
| 1.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0
1 VM | 2573.9 | 9832.8 | 15807.4 | 21068.6 | 23549.3 | 24377.4 | 24526.6
8 VM | 20915 | 48186.8 | 60950.3 | 73298.5 | 80371.8 | 83242.3 | 83443.6
Topology | Session | 1 VM | 8 VMs
vlan | 64 | 26 KCPS | 113 - 118 KCPS
stt | 64 | 25 KCPS | 83 - 115 KCPS
vxlan | 64 | 24 KCPS | 81 - 85 KCPS
Note: results are for the ‘application-layer’ topology
Multiple concurrent flows

## Slide 33: Summary
Have a well-established test framework and methodology
Evaluate performance at different layers
Understand variations
Collect all relevant hw details and configuration settings

## Slide 34
Thank You!