## Slide 1: Enabling TSO in OvS-DPDK
Tiago Lam
Intel
December 5th-6th, 2018 | San Jose, CA

## Slide 2: Agenda
What is TSO?
Why TSO in Userspace DPDK?
Enable TSO in Userspace DPDK
Performance results
Considerations
Status and future work

## Slide 3: TSO (TCP Segmentation Offload)
TSO is the segmentation of large chunks of data, relative to the MTU, into smaller segments, performed by the network NIC;
C
S
Segmentation
Checksum
DATA
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
C
C
S
C

## Slide 4: Why TSO in Userspace DPDK?
OvS-DPDK
Host 1
VM1
NIC
Intra-host
Inter-host
VM2
OvS-DPDK
Host 2
VM1
NIC
VM2

## Slide 5: Non TSO overview
eth0
NIC
dpdk0
vhuc0
VM OS Kernel
VM OS Userspace
DATA
IP
TCP
DATA
IP
TCP
DATA
IP
TCP
DATA
Application Layer
TCP/IP Layers
Link Layer
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
Host OS Userspace
vhuc1
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
Intra-host
VM1
VM2
Host 1
Host 2
Inter-host
OvS-DPDK

## Slide 6: The cost of non TSO
Higher CPU loads;
Lower overall throughput:
  More noticeable in Intra-host.
DATA
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
C
C
S
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
C
S
Segmentation
Checksum
C

## Slide 7: TSO in Userspace DPDK

## Slide 8: Single-segment mbufs
Used in master OvS-DPDK (<=2.10);
Mbufs allocated with the maximum packet size (e.g. 9KiB);
No flexibility to hold different sized packets.
ETH
IP
TCP
DATA
Mbuf struct
ETH
IP
TCP
DATA
Mbuf struct

## Slide 9: A case for multi-segment mbufs
Mbufs allocated with a default size (2k);
Chained together if needed to hold bigger packets;
ETH
IP
TCP
DATA
Mbuf struct
Mbuf struct
DATA
Mbuf struct
DATA

## Slide 10: A case for multi-segment mbufs
Mbufs allocated with a default size (2k);
Chained together if needed to hold bigger packets;
Data is no longer held
contiguously in memory:
struct ip_header *ip;
…
if (OVS_UNLIKELY(!dp_packet_ip_checksum_valid(packet))) {
if (csum(ip, IP_IHL(ip->ip_ihl_ver) * 4)) {
VLOG_WARN_RL(&err_rl, "ip packet has invalid checksum");
return NULL;
}
}
…
ETH
IP
TCP
DATA
Mbuf struct
Mbuf struct
DATA
Mbuf struct
DATA

## Slide 11: A case for multi-segment mbufs
VM1
NIC
VM2
OvS-DPDK
vhuc0
vhuc1
ETH
IP
TCP
DATA
Mbuf struct

## Slide 12: TSO integration
Set mbuf’s layer l2_len, l3_len and l4_len fields;
l3_len=0x14
l2_len=0x0e
ETH
IP
TCP
DATA
Mbuf struct
l4_len=0x14
mbuf

## Slide 13: TSO integration
Set mbuf’s layer l2_len, l3_len and l4_len fields;
Mark packet for offload with flags:
  PKT_TX_IPV4 | PKT_TX_IP_CKSUM;
  PKT_TX_TCP_SEG | PKT_TX_TCP_CKSUM.
ETH
IP
TCP
DATA
Mbuf struct
l3_len=0x14
l2_len=0x0e
l4_len=0x14
ol_flags=PKT_TX_IPV4 | PKT_TX_IP_CKSUM |
PKT_TX_TCP_CKSUM | PKT_TX_TCP_SEG;
mbuf

## Slide 14: TSO integration
Set mbuf’s layer l2_len, l3_len and l4_len fields;
Mark packet for offload with flags:
  PKT_TX_IPV4 | PKT_TX_IP_CKSUM;
  PKT_TX_TCP_SEG | PKT_TX_TCP_CKSUM.
Set the TSO segment size;
ETH
IP
TCP
DATA
Mbuf struct
l3_len=0x14
l2_len=0x0e
l4_len=0x14
tso_segsz=$mtu - l3_len - l4_len
ol_flags=PKT_TX_IPV4 | PKT_TX_IP_CKSUM |
PKT_TX_TCP_CKSUM | PKT_TX_TCP_SEG;
mbuf

## Slide 15: TSO integration
Set mbuf’s layer l2_len, l3_len and l4_len fields;
Mark packet for offload with flags:
  PKT_TX_IPV4 | PKT_TX_IP_CKSUM;
  PKT_TX_TCP_SEG | PKT_TX_TCP_CKSUM.
Set the TSO segment size;
Prepare packet for tx offload:
  rte_eth_tx_prepare();
* Note: In older versions of DPDK checksum calculations differ between NICs / replaced by rte_eth_tx_prepare();
l3_len=0x14
l2_len=0x0e
ETH
IP
TCP
DATA
Mbuf struct
l4_len=0x14
ipv4_hdr->hdr_checksum=0;
tcp_hdr->cksum=rte_ipv4_phdr_cksum(ipv4_hdr, mbuf->ol_flags);
tso_segsz=$mtu - l3_len - l4_len
ol_flags=PKT_TX_IPV4 | PKT_TX_IP_CKSUM |
PKT_TX_TCP_CKSUM | PKT_TX_TCP_SEG;
mbuf

## Slide 16: Intra-host with TSO
Lower CPU loads;
Higher overall throughput.
NIC
VM1 / OvS-DPDK / VM2
1
2
3
C
S
Segmentation
Checksum
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
ETH
IP
TCP
DATA
C
C
S
ETH
IP
TCP
DATA
OvS-DPDK
Host 1
VM1
NIC
VM2
2
1
3
S
C
C

## Slide 17: Performance results
Chart: Gbps
| Intra-Host | Inter-Host
Master | 5.5 | 5.22
TSO | 32.3 | 9.22
In-Kernel | 25.9 | 9.34

## Slide 18: Considerations
No vectorized optimizations:
  Found to affect 64B packets only.
DPDK v17.11 vs v18.11:
  Better support to query devices on offload capabilities.
Contiguous vs non-contiguous memory;
No GSO fall-back;

## Slide 19: Status and future work
Two patches submitted upstream:
  Add support for multi-segment mbufs [1];
  Add support for TSO (RFC) [2].
Focus on getting multi-segment mbufs upstreamed;
GSO support.

## Slide 20: Thanks!

## Slide 21: References
[1] https://mail.openvswitch.org/pipermail/ovs-dev/2018-October/352889.html
[2] https://mail.openvswitch.org/pipermail/ovs-dev/2018-August/350832.html

## Slide 22: Notices & Disclaimers
Intel technologies’ features and benefits depend on system configuration and may require enabled hardware, software or service activation. Performance varies depending on system configuration. Check with your system manufacturer or retailer or learn more at intel.com.
No computer system can be absolutely secure.
Tests document performance of components on a particular test, in specific systems. Differences in hardware, software, or configuration will affect actual performance. Consult other sources of information to evaluate performance as you consider your purchase. For more complete information about performance and benchmark results, visit http://www.intel.com/benchmarks .
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit http://www.intel.com/benchmarks .
Intel's compilers may or may not optimize to the same degree for non-Intel microprocessors for optimizations that are not unique to Intel microprocessors. These optimizations include SSE2, SSE3, and SSSE3 instruction sets and other optimizations. Intel does not guarantee the availability, functionality, or effectiveness of any optimization on microprocessors not manufactured by Intel. Microprocessor-dependent optimizations in this product are intended for use with Intel microprocessors. Certain optimizations not specific to Intel microarchitecture are reserved for Intel microprocessors. Please refer to the applicable product User and Reference Guides for more information regarding the specific instruction sets covered by this notice.
Cost reduction scenarios described are intended as examples of how a given Intel-based product, in the specified circumstances and configurations, may affect future costs and provide cost savings. Circumstances will vary. Intel does not guarantee any costs or cost reduction.
Intel does not control or audit third-party benchmark data or the web sites referenced in this document. You should visit the referenced web site and confirm whether referenced data are accurate.
© 2018 Intel Corporation.
Intel, the Intel logo, and Intel Xeon are trademarks of Intel Corporation in the U.S. and/or other countries.
*Other names and brands may be claimed as property of others.

## Slide 23: Backup

## Slide 24: Test setup
Host:
  OS: Ubuntu 16.04.2 LTS - 4.10.0-28-generic
  NIC1: Intel X710 10-Gigabit Ethernet Controller
  NIC2: Intel 82599ES 10-Gigabit Ethernet Controller
VMs: Fedora 27 - 4.15.14-300.fc27.x86_64
QEMU: version 2.5.0
Iperf: version 2.0.11
OvS: v2.10
DPKD: v17.11.3