## Slide 1: Reprogrammable packet processing pipeline
__________________________________
December 5, 2018
Debashis Chatterjee

## Slide 2: Agenda
Intro to Glaciers
A network parse graph
Need for programmable packet processing pipeline
Intel’s reprogrammable parser
Parser tools flow
Intel’s reprogrammable modifier
SDK and SW stack
Q&A

## Slide 3
Mt Kiska product family - Cascade Glacier
Programmable vSwitch Offload
  Open vSwitch and other vSwitches
  High speed Internal Switch Fabric
  Millions of flows
  Connection tracking & other features
Embedded CPU Cores
  vSwitch slow path & NIC management
Virtio-net Hardware Offload
  Supports Existing Linux & DPDK VMs
  Multiple queues per device
  Live migration between HW & SW
PCI, SR-IOV
25GbE
Ethernet
25GbE
Ethernet
vNIC
VF
vNIC
VF
Programmable vSwitch Pipeline
DDR4 Memory Controller
Cascade Glacier
FPGA
ARM

## Slide 4: Packet processing parse graph
Packet Parser
Packet Filters
What packet is this?
TCP or UDP or TCP in VXLAN?
1
3
2
5
4
10
9
Ethernet
IP
VLAN
IPv4
IPv6
TCP
UDP
6
8
7
12
11
IP
IPv4
IPv6
TCP
UDP
Packet type = 1->2->6->8->11 = Some number ‘P1’
Table 1
Forward = To VSI, Mirror
Crypto = IPsec Tunnel mode, Transport, DTLS
Encap = VXLAN, NVGRE, MPLS
Update = IP TTL, Checksum, NAT
Telemetry= packets, bytes
Sample = To PF, remote system
Packet type | Header Fields | Actions
P1 | VLAN, SIP, DPORT | VF(4), RATE LIMIT
P1 | VLAN, SIP, DPORT | VF(14), RATE LIMIT, SAMPLE
P2 | VLAN, DIP, DPORT, SPORT | DROP, SAMPLE
P3 | VLAN, SIP, DPORT | VF(112), MIRROR
wire
host
Table 2
Packet type | Header Fields | Actions
P1 | DIP, SIP, DPORT | ENCRYPT, ENCAP
P3 | SIP, DPORT,SPORT | ENCRYPT, ENCAP, NAT
P3 | SIP, DPORT,SPORT | ENCRYPT, ENCAP, NAT
P7 | SIP, DPORT,SPORT , SMAC | ENCAP, SAMPLE
Packet Modifier
Egress
Scheduler
Packet type = 1->2->6->8->12 = Some number ‘P2’

## Slide 5: Need for programmable packet processing pipeline
OpenFlow experience
A packet classifier uses values of different header fields for state transitions
A hardened ASIC implementation of an OpenFlow classifier would have to go through anywhere from a multi-layer change to just a metal fix to accommodate these. Cost of even a metal fix at 14 nm could be hundreds of thousands of dollars
CSPs often experiment with pre-RFC protocols
Overriding header fields with new interpretations is also not uncommon
 |  | Header Fields
Version | Date | 
OF 1.0 | Dec-09 | 12 fields (Ethernet, TCP/IPv4)
OF 1.1 | Feb-11 | 15 fields (MPLS, inter-table metadata)
OF 1.2 | Dec-11 | 36 fields (ARP, ICMP, IPv6, etc.)
OF 1.3 | Jun-12 | 40 fields
OF 1.4 | Oct-13 | 41 fields

## Slide 6: Intel’s reprogrammable parser
Eth
IPv4
IPv6
Ethtype = 0x800?
Ethtype = 0x86DD?
TCP
UDP
Protocol = 0x6?
Protocol = 0x11?
@protocol_id("IPV4") @name("parse_ipv4") state parse_ipv4 {
packet.extract(hdr.ipv4[0]);
transition select(hdr.ipv4[0].protocol) {
8w0x11: parse_udp;
8w0x6: parse_tcp;
8w0x1: parse_icmp;
8w0x2f: parse_gre;
default: accept;
}
}
hdrOffset | cmpFldType | cmpFldEn[0] | cmdFldOffset[0] |  | cmpFldEn[1] | cmdFldOffset[1]
0 | CMP_VLAN | 1 | 36 |  | 0 | 0
cmpFldIdx | cmpFldType | cmpFldEn[0] | cmpFld[0] | cmpFldMask[0] | cmpFldEn[1] | cmpFld[1]
0 | CMP_VLAN | 1 | 0x800(ipv4) | 0xFFFF | 0 | 0
1 | CMP_VLAN | 1 | 0x86dd(ipv6) | 0xFFFF | 0 | 0
2 | CMP_VLAN | 1 | 0x806(arp) | 0xFFFF | 0 | 0
3 | CMP_VLAN | 1 | 0 | 0 | 0 | 0

## Slide 7: Parser tools flow
P4 source
P4 to parser binary generator
Binary Table
Optional Virtual platform to test and debug
Customer
Cascade Glacier

## Slide 8: Intel’s reprogrammable modifier
General
  Designed like a programmable CPU, with opcodes representing actions such as DEC_TTL, ENCAP, DECAP, CKSUM etc
  A modifier action template has the action to be taken along with associated data
  Modifier templates are downloaded to modifier memory by a tool similar to parser tool
Decap
  Driven by a ‘template’ provided by the classifier
  Removes some number of bytes from header
Mod
  Pulls data from DDR4 and small on-die tables
  Driven by a ‘template’ provided by the classifier
  Updates some number of bytes in the header
  Provides checksums, length adjustments for IP/L4
Encap
  Pulls data from DDR4 & small on-die tables
  Driven by a ‘template’ provided by the classifier
  Adds some number of bytes to the header
  Provides checksums, length adjustments for new IP/L4
Intel Confidential - Presented Under CNDA

## Slide 9
Cascade Glacier SDK and SW stack
Linux
Flow APIs
Standard Virtio-net driver
Mgmt driver
NIC Tools
iproute2 ethtool
SDK APIs
Open vSwitch or Custom
OpenStack
OpenStack Agent or Custom
CG
SDK
PF driver
Firmware binaries
Sample code
Pipeline reconfigurator
Mgmt. driver
Diagnostic tools
Setup scripts
API library