## Slide 1: Converting OpenFlow to P4
James Choi, Intel
Intel P4-OVS Team: Dan Daly, Anjali Singhai, James Choi, P. Venkata Suresh Kumar, Namrata Limaye, Debashis Chatterjee

## Slide 2: Notices & Disclaimers
Performance varies by use, configuration and other factors. Learn more at www.Intel.com/PerformanceIndex.
Performance results are based on testing as of dates shown in configurations and may not reflect all publicly available updates. See backup for configuration details. No product or component can be absolutely secure.
Your costs and results may vary.
Intel technologies may require enabled hardware, software or service activation.
© Intel Corporation. Intel, the Intel logo, and other Intel marks are trademarks of Intel Corporation or its subsidiaries. Other names and brands may be claimed as the property of others.

## Slide 3: Agenda
Offloading to datapath pipeline
OpenFlow optimization difficulties
P4 as a solution
Elements of a P4 program
OpenFlow to P4 mapping steps
OpenFlow to P4 mapping basic steps
OpenFlow to P4 mapping next steps
Summary

## Slide 4: Offloading to Datapath Pipeline

## Slide 5: OpenFlow optimization difficulties
Difficulties with optimizing OpenFlow
No explicit control flow mechanism in OpenFlow
  No explicit statements like if-else to control table rule evaluation sequence. Priority based control flow is too simplistic.
  Implicit control flow rule entries in a table is obfuscated by other lookup rule entries
No limit on match key field that can be used on-the-fly for a rule
  Hard to optimize for unknown set of rules keys to optimize for implementation
No limit on set of action sequences that can be used
  Hard to optimize for unknown set of rule action sequences
Difficulties with offloading network flows from OpenFlow
Devices offload datapath flows in generic sub-optimal ways
Difficult to take advantage of specialized SW algorithms or HW blocks for specific networking functions with OpenFlow alone.

## Slide 6: P4 as a solution
P4 provides a way for OVS to offload OpenFlow table more optimally through mapping of OpenFlow tables to P4 tables.
A P4 program describes data-plane pipeline in more precise way, which make it easier to optimize.
The order of table evaluation is explicitly defined
The lookup key fields and actions are defined to only for desired fields and sequence of actions.
Compilers can be utilized map P4 tables to target dataplane optimally
Mapping of OpenFlow to P4 needs to be done manually along with programming of P4 tables and control flows.
Advantages of offloading P4 tables
Enables offloading specific P4 tables to specialized SW algorithms or HW blocks
Scale of entries in P4 tables are same as in the tables in controller DB
Change to a rule in P4 table is immediately applied to data-plane, not requiring separate OpenFlow rule evaluation

## Slide 7: Elements of a P4 program
control Sample (…)
{
action route (nexthop_mac, port) {
hdr.eth_src = nexthop_mac;
md.egress_port = port;
}
action drop() { … }
table l3_lookup {
key = {
hdr.ipv4.dst_addr : lpm;
}
actions = {
route;
drop;
}
}
table l2_lookup {
key = {
hdr.eth.dst_mac : exact;
}
}
apply {
if ( hdr.ipv4.isValid() ) {
l3_lookup.apply();
}
else {
l2_lookup.apply();
}
}
}
Precise sequence of actions
grouped together like a profile
Specific set of possible actions per table.
Specific fields used for match keys and
specific type of lookup to be done for
each table
Explicit control flow statements
to control table lookups

## Slide 8: OpenFlow to P4 mapping steps

## Slide 9: OpenFlow to P4 mapping basic steps
Identify P4 lookup tables from CMS DB
    Identify precise encoding of the keys that reflects the intended use of each lookup table.
P4 control flow and P4 actions from OpenFlow DB tables
    Identify precise encoding of P4 actions that reflects only the sequence of actions used for each table
    Identify annotation for each OF rule to a P4 table and P4 action
Compile P4 program with a P4 compiler with targeted SW or HW pipeline backend support
Load compiler output to P4 OVS and device
  Load P4 dataplane information to P4 supported datapath
  Load P4 runtime information to P4 OVS
  Load P4-to-pipeline mapping information to P4 support SDK/API
Configure P4 OVS OpenFlow rules with identified annotations for P4 tables and P4 actions
These steps are sufficient to start running with OpenFlow to P4 mapped pipeline.

## Slide 10: OpenFlow to P4 mapping next steps
Integrate P4 into SDN controller that originates OpenFlow messages (e.g. ovn-controller)
  Support integrating P4 runtime information into controller
  Update table entries in OpenFlow DB with P4 table and P4 action mapping information
Encode the mapping info in OpenFlow messages
Integrate P4 into SDN controller that populates OpenFlow DB from CMS DB
Integrate P4 Runtime into SDN controller
Use P4 Runtime between P4 driven controller and P4 OVS

## Slide 11: Summary
P4 can encode your pipeline better. Ideally you would have your controller talk P4 Runtime, but there is also an approach where you can use P4 for the dataplane and continue to use OpenFlow as an RPC between controller and vSwitch. This can be done by mapping OpenFlow entries to P4 tables with annotations
The integration of P4 into controllers and using P4 Runtime is the ideal way to support P4 driven OVS; however, it can be done as a next step.
Initial support for P4 OVS using OpenFlow can start with basic changes in OVS only
P4 can be used to encode the intent of controller table usage in OVS to optimize offloading flows.
Manual programming of P4 program and mapping of OpenFlow to P4 is needed.
More talks on Intel P4-OVS are available:
  p4proto: Cooking OVS with P4 Spice! (Namrata Limaye and Deb Chatterjee)
  vswitch.p4: Why OVS Needs P4 (Dan Daly)